## Slide 1: Influence of Tractor Speed and Boom Height on Spray Coverage
Eric P. Prostko1, Glen C. Rains2, and O. Wen Carter1
1Dept. Crop & Soil Sciences
2Dept. of Entomology
UGA - Tifton

## Slide 2
The New Norm????

## Slide 3: Is this a bad combination????
6 ft

## Slide 4: Farm vs. Research?
Concerns
Tractor Speed
Boom Height
Coverage
Quality vs. Quantity?

## Slide 5: Herbicide Efficacy
Chart: 
| Rate | Timing | Environment | Coverage
Column1 | 0.25 | 0.25 | 0.25 | 0.25
Coverage
Nozzle Type
GPA
Pressure
Boom Height
Tractor Speed

## Slide 6: Objective
Evaluate the effects of tractor speed and boom height on spray quality
  Coverage
  VMD50

## Slide 7: Materials and Methods
Melroe 3430 Spra-Coupe
Tractor Speeds
  4.4, 6.5, and 9.5 MPH
Boom Heights
  30, 45, 60 in
  Wind ≤ 3.0 MPH
15 GPA (water + dye)
DG TeeJet Drift Guard Nozzle Tips (20” spacing)
  8002DG (50 PSI)
  8003DG (40 PSI)
  8004DG (53 PSI)
    Medium Droplet Sizes
2 locations in sprayer path
  8’ from tractor center (L1)
  30” parallel from L1 (L0)
5 Kromekote cards (2” X 3”)
  10’ apart
Dropletscan (WRK of Arkansas, LLC)

## Slide 8: Droplet Size - TeeJet

## Slide 9
10’
30”
8’

## Slide 10: Results
Analyzed data as 2 X 3 X 3 factorial
  2 card locations
    5 cards
  3 speeds
  3 boom heights
90 total data points
Speed X Boom Height interaction for Coverage and VMD50

## Slide 11: Influence of Tractor Speed and Boom Height on Spray Coverage (%)
Chart: Boom Height (in)
| 30 | 45 | 60
4.4 MPH | 12 | 10 | 12
6.5 MPH | 11 | 10 | 10
9.5 MPH | 6 | 8 | 6
LSD 0.10 = 1
CV = 12.523

## Slide 12: Tractor Speed Effects on Spray Coverage (%) – 30” Boom Height
Chart: Speed (MPH)
| 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5
Y-Values | 10 | 12 | 12 | 9 | 10 | 12 | 12 | 14 | 13 | 15 | 9 | 11 | 12 | 8 | 9 | 9 | 13 | 12 | 12 | 12 | 7 | 5 | 6 | 5 | 4 | 7 | 7 | 6 | 6 | 7
N = 30

## Slide 13: Tractor Speed Effects on Spray Coverage (%) – 45” Boom Height
Chart: Speed (MPH)
| 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5
Y-Values | 10 | 7 | 11 | 9 | 10 | 9 | 10 | 9 | 12 | 12 | 9 | 9 | 9 | 12 | 7 | 11 | 12 | 13 | 10 | 9 | 7 | 6 | 7 | 6 | 5 | 8 | 9 | 9 | 8 | 11
N = 30

## Slide 14: Tractor Speed Effects on Spray Coverage (%) – 60” Boom Height
Chart: Speed (MPH)
| 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 4.4000000000000004 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5
Y-Values | 10 | 9 | 14 | 10 | 10 | 12 | 12 | 13 | 11 | 15 | 9 | 7 | 11 | 8 | 8 | 10 | 12 | 11 | 11 | 12 | 5 | 6 | 6 | 4 | 5 | 4 | 8 | 8 | 6 | 4
N = 30

## Slide 15: Spray Coverage - 60” Boom Height
4.4 MPH
6.5 MPH
9.5 MPH

## Slide 16: Influence of Tractor Speed and Boom Height on Droplet Size (VMD50)
Chart: Boom Height (in)
| 30 | 45 | 60
4.4 MPH | 316 | 311 | 306
6.5 MPH | 324 | 328 | 329
9.5 MPH | 345 | 325 | 321
LSD 0.10 = 5
CV = 1.83
Medium =
236-340 VMD50

## Slide 17: Summary – Tractor Sprayer
Lowest coverage at all boom heights was at 9.5 MPH tractor speed (6-8%)
For 30” and 60” boom heights, negative linear relationship between tractor speed and coverage (R2 > 0.68)
  ~ 1.2% loss in coverage for each MPH
Boom height influenced spray coverage as follows:
  4.4 MPH: 30” = 60” > 45”
  6.5 MPH: 30” = 45” = 60”
  9.5 MPH: 45” > 30” = 60”
Generally, VMD50 increased with tractor speed
  30” boom: 4.4 MPH < 6.5 MPH < 9.5 MPH
  45” boom: 4.4 MPH < 6.5 MPH = 9.5 MPH
  60” boom: 4.4 MPH < 9.5 MPH < 6.5 MPH
  306 to 345 microns (coarse droplet size)

## Slide 18: BackPack Sprayer Coverage Evaluation
Generally, same MM as tractor study
September 1, 2015
15 GPA
3 nozzle boom, 20” spacing
20” Boom Height
3.5 MPH (walking)
Wind (<1 MPH)
35-40 PSI
3 nozzle types
  11002DG
  AIXR 11002
  TTI02

## Slide 19: The Influence of Nozzle Type on Spray Coverage (%) and VMD50 (microns)
Chart: 
| 11002DG | AIXR 11002 | TTI02
Coverage (%) | 13.4 | 12.6 | 9.5
Chart: VMD50 (microns)
| 11002DG | AIXR11002 | TTI02
VMD50 | 322 | 402 | 524
3.5 MPH - Walking
20” nozzle spacing
20” boom height
35-40 PSI
15 GPA
LSD 0.10 = 1.8
CV = 18.3
LSD 0.10 = 19
CV = 6

## Slide 20
11002DG
VMD50 = 322 (C
AIXR 11002
VMD50 = 402 (VC)
TTI 02
VMD50 = 524 (XC)

## Slide 21: Final Thoughts
If a grower would drive 4.4-6.5 MPH, not much difference between backpack and tractor.
If grower drives 9.5 MPH or greater (?), ~50% less spray coverage.
Could this partially explain observed differences between research and on-farm results???
Farmer Resistance?
  Too big/late, too fast, too high?????

## Slide 22: Acknowledgements
Technical Support provided by
  Tim Richards
  Charlie Hilton
  Maryssa Davis

## Slide 23
QUESTIONS?
eprostko@uga.edu
www.gaweed.com